## Slide 1: Diffusion Tensor Imaging Analysis
Feb 1, 2023

## Slide 2: What is DTI?
Measuring the movement of water

## Slide 3: What is DTI?

## Slide 4: DTI Data Collection
Important parameters:
  Number and value of B(s)
  # gradient directions
For Elition we have 3 suggested DTI sequences (see Dec meeting on Vbrain sequences)
  HARDI 60
  98 direction / 3 Bs
  128 direction / 3 Bs

## Slide 5: Analysis Pipelines
Depending on how you collect you data, you can use different analysis techniques.
For more advanced modelling, multi-shell diffusion (a few B values) is needed
To correct for image distortion due to EPI, need to collect B0 scans with opposite phase

## Slide 6: Basic Analysis
For basic analysis I like to use FSL processing
- great wiki reference (and links within) at https://fsl.fmrib.ox.ac.uk/fsl/fslwiki/FDT/UserGuide#Processing_pipeline
Convert data (PAR/REC or dicom) to .nii using dcm2niix
  - This should result in 4 files: .nii, .json, .bval, .bvec
Grab the B0 image(s)
  fslroi DTI.nii B0.nii 0 1
Depending on if you do distortion corrections, the next steps are different.

## Slide 7: Topup or no Topup?
Topup corrected
Reverse phase
B0 image

## Slide 8: No Topup
3. Brain extract the B0
> bet B0.nii B0_brain –f 0.2 –g 0 –m
4. Create acqparam and index files
> acqparam.txt describes images in DTI file (specifying the phase-encoding direction). Index.txt links acqparam and DTI files.
5. Do eddy current correction
> eddy_openmp --imain=DTI --acqp=acqparams.txt --index=index.txt –mask=B0_brain_mask --bvals=…bval --bvecs=…bvec --out=DTI_NO_TU
6. Run tensor analysis
> dtifit --data=DTI_NO_TU --out=DTI --mask=mask=B0_brain_mask --bvals=…bval --bvecs=DTI_NO_TU.eddy_rotated_bvecs

## Slide 9: Using TopUp
3. Merge B0
  > fslmerge –t DTI_b0_all DTI_b0 DTI_reverse
4. Find Topup values
> topup --imain=DTI_b0_all --datain=acqparams.txt --config=b02b0.cnf --out=topup_PA_AP_b0 --fout=topup_PA_AP_b0_field --iout=topup_PA_AP_b0_unwrapped
5. Apply topup
> applytopup --imain=DTI_b0,DTI_reverse --inindex=1,2 --datain=acqparams.txt --topup=topup_PA_AP_b0 --out=topup_hifi_nodiff
6. BET
> bet topup_hifi_nodiff topup_hifi_nodiff_brain -m -f 0.2
7. Eddy current correct
> eddy_openmp --imain=DTI --mask=topup_hifi_nodiff_brain_mask --datain=acqparams.txt --index=index.txt --bvals=…bval --bvecs=…bvec --out=ECC --ref_scan_no=0 --ol_nstd=4 --topup=topup_PA_AP_b0
8. Run tensor analysis
> dtifit --data=ECC --out=DTI --mask=topup_hifi_nodiff_brain_mask --bvals=…bval --bvecs= ECC.eddy_rotated_bvecs

## Slide 10: Acqparams and Index files
Acqparams refers to how the data was acquired (one line for each B0 image)
0 -1 0 0.01
0 1 0 0.01
Index file links the imain file to the acqparams file
  single row with 1 entry per volume in imain pointing to which line of acqparams it was acquired as
  > fslnvols DTI (can help determine how many entries in index)
first 3 entries are direction of phase encoding, last is total readout time

## Slide 11: Issues with topup
It seems that the config file b02b0.cnf expects the DTI file to have an even number of slices.
FMRIB has now created other config files:
  b02b0_4.cnf -- data is multiple of 4 in all directions
  b02b0_2.cnf -- data is multiple of 2 in all directions
  b02b0_1.cnf -- data is odd in one or more directions

## Slide 12: What is output?
After running dtifit, you get 10 parameter files:
  3 eigenvalues (L1, L2, L3)
  3 eigenvectors (V1, V2, V3)
  fraction anisotropy (FA)
  mean diffusivity (MD)
  mode of the anisotropy (M0)
  raw T2 signal with no diffusion weighting (S0)

## Slide 13: Now what?
Get mean and standard deviation values from an ROI
  > fslstats DTI_XX.nii.gz -k ROI.nii.gz -m -s
Parameters of interest
FA - measures degree of anisotropy (0=iso, 1=aniso)
MD - average diffusion measure
L1 - axial diffusivity (along tract direction)
Average (L2, L3) - radial diffusivity (perpendicular to axon)

## Slide 14: Tractography
By following the principal diffusion direction, we can map the length of a fibre tract.

## Slide 15: Tractography
In FSL, first run BEDPOSTX then PROBTRACKX
  > bedpostx subject_directory
  (the directory will need to contain bval and bvec files, data file, brain mask)
  (expect BEDPOSTX to run a long time)
> probtrackx -s basename -m maskfile -x seedfile -o output
These commands can also be run within the FSL GUI which may be more straightforward.

## Slide 16: Multi-B shell modeling
A number of different approaches
  DBSI (Diffusion Basis Spectrum Imaging)
  NODDI (Neurite Orientation Dispersion and Density Imaging)
  DKI (Diffusion Kurtosis Imaging)
  …

## Slide 17: Next meeting
March 1st