## Slide 1: ANTs
UBC MRI Research Analysis Meeting
Oct 4, 2023

## Slide 2: What is ANTs
Advanced Normalization Tools
popularly considered a state-of-the-art medical image registration and segmentation toolkit
Uses ITK
Find info at: https://stnava.github.io/ANTs/

## Slide 3: Some uses of ANTs
Registration
Segmentation
Functional image analysis
Cortical Thickness
Template Creation
…

## Slide 4: Some uses which I will focus on
Bias Field Correction
Brain Extraction
Registration
  Pairwise
  Atlas
Cortical Thickness

## Slide 5: Bias Field Correction
Used to correct intensity differences across image
N4BiasFieldCorrection -d 3 -i filename.nii.gz -o outfilename_N4.nii.gz

## Slide 6: Brain Extraction
Considered one of the better tools for this
Templates can be found at: https://figshare.com/articles/dataset/ANTs_ANTsR_Brain_Templates/915436
ANTsPyNet
antsBrainExtraction.sh -d 3 -k 1 -z 0 -a T1w_file_N4.nii.gz -e …/OASIS/T_template0.nii.gz -m …/OASIS/T_template0_BrainCerebellumProbabilityMask.nii.gz -f …/OASIS/T_template0_BrainCerebellumRegistrationMask.nii.gz -o outfile_BET.nii

## Slide 7: Registration
Was the original goal of ANTs
antsRegistrationSyNQuick
antsRegistration
antsApplyTransforms
antsMultivariateTemplateConstruction2

## Slide 8: Quick registration
antsRegistrationSyNQuick.sh -d 2 -f B.nii.gz -m A.nii.gz -o RegA2B
Optional
-n: number of threads (default = 2)
-t: transform type (default=‘b’)
  t: translation
  r: rigid
  a: rigid+affine
  s: rigid+affine+deformable syn
sr: rigid+deformable syn
b: rigid+affine+deformable b-spline syn
br: rigid+deformable b-spline syn

## Slide 9: Registration
antsRegistrationSyN -d dimension -f Fixed.nii -m Moving.nii -o OutputPrefix
Optional
  -n: # threads
  -t: transform type
    same as previous slide plus so: deformable syn only and bo: deformable b-spline syn only
  -r: radius for cross correlation matrix (default=4)
  -s: spline distance (default=26)
  -g: gradient step size (default=0.1)
  -x: mask for fixed image space
  ...

## Slide 10: Apply Transforms
Affine
antsApplyTransforms -i input.nii -r destination.nii -t GenericAffine.mat -o WarpedOutput_Affine.nii -n InterpolationMethod
Diffeomorphic + Affine
antsApplyTransforms -i input.nii -r destination.nii -t GenericAffine.mat -o WarpedOutput_Diff_Affine.nii -n InterpolationMethod -u Warp.nii

## Slide 11: Registration similarity metric
Used to determine best registration
  Cross correlation estimate: -m CC[fixedImage,movingImage,weight,radius]
  Mutual Information: -m MI[fixedImage,movingImage,weight,number-of-histogram-bins,samplingStrategy,samplingPercentage]
  Global correlation: -m GC[fixedImage,movingImage,weight,0, samplingStrategy,samplingPercentage]
  Mean square difference: -m MeanSquares[fixedImage,movingImage,weight,0]

## Slide 12: Pairwise registration
Registers 2 images to a halfway space
unbiased_pairwise_registration.sh -d dimension -f fixed.nii -m moving.nii -o OutputPrefix
Script may not be in regular ANTs download so can get at
https://github.com/ANTsX/ANTs/blob/master/Scripts/unbiased_pairwise_registration.sh

## Slide 13: Template creation
antsMultivariateTemplateConstruction2.sh -d dimension -o OutputPrefix <ListOfImages>
Optional
  -i: iterations (4)
  -g: gradient (0.15)
  -c: cores (2)
  -j: # CPU cores
  -k: number of modalities (1)
  -w: modality weights used (1)
  -f: shrink factors (6x4x2x1)
Output average template image called {OutputPrefix}template0.nii.gz
-s: smoothing (3x2x1x0)
-q: max interations (100x100x80x40)
-n: bias field correction (1=on)
-y: update template with affine (1)
-r: do rigid reg before main reg (1)
-m: type of similarity matrix (CC)
-l: use linear reg for pairwise (1)
-t: type of transformation (SyN)

## Slide 14: Cortical Thickness
antsCorticalThickness.sh -d dimension -a T1.nii -e …/OASIS/T_template0.nii.gz -t …/OASIS/T_template0_BrainCerebellum.nii.gz -m …/OASIS/T_template0_BrainCerebellumProbabilityMask.nii.gz -f …/OASIS/T_template0_BrainCerebellumExtractionMask.nii.gz -p …/OASIS/Priors2/priors%d.nii.gz -q 1 -o OutputPrefix

## Slide 15: Motion Correction
# average the time series
antsMotionCorr -d 3 -a input.nii -o output_avg.nii.gz
# do affine motion correction
antsMotionCorr -d 3 -o [OutputPrefix,output.nii.gz,output_avg.nii.gz] -m gc[ output_avg.nii.gz , input , 1 , 1 , Random, 0.05] -t Affine[ 0.005 ] -i 20 -u 1 -e 1 -s 0 -f 1 -n 10
# do affine and deformable correction
antsMotionCorr -d 3 -o [OutputPrefix,output.nii.gz,output_avg.nii.gz] -m gc[ output_avg.nii.gz , input , 1 , 1 , Random, 0.05] -t Affine[ 0.005 ] -i 20 -u 1 -e 1 -s 0 -f 1 -m CC[output_avg.nii.gz , input , 1 , 2 ] -t GaussianDisplacementField[0.15,3,0.5] -i 20 -u 1 -e 1 -s 0 -f 1 -n 10

## Slide 16: Other scripts available in ANTs
antsASLProcessing.sh
DenoiseImage
LesionFilling
statistics

## Slide 17: Next Meeting
Next meeting: Nov 1st
Topic: suggestions welcome