## Slide 1: Imaging of Neurofluids
Irene Vavasour
Dec 3, 2025
UBC MRI Research Centre Monthly Analysis Meeting

## Slide 2: Land Acknowledgment
I would like to acknowledge that UBC’s Point Grey campus is situated on the traditional, ancestral and unceded territory of the Musqueam people.
To learn more about our indigenous communities visit
  https://medicine.med.ubc.ca/indigenous-resources/

## Slide 3: Neurofluids
all fluids in brain and spinal cord
  arterial blood
  venous blood
  cerebrospinal fluid (CSF)
  interstitial fluid (ISF)

## Slide 4: Glymphatic system
brain-wide neurofluid exchange network that facilitates waste clearance
Szlufik S. Cells 2024

## Slide 5: Components of the Glymphatic System

## Slide 6: Neurovasculature
prevents reductions in blood flow during drops in blood pressure
matches delivery of oxygen and glucose with brain energy requirements
contributes to clearance of metabolic waste generated by the brain
regulates bidirectional molecular exchange between blood and brain through transcytosis and molecular transporters
is involved in the trafficking of immune cells in and out of the brain
generates growth factors to maintain neurons and glia

## Slide 7: Perivascular Spaces
space between the outer aspect of an artery wall and the brain parenchyma
visible on MRI as small lines or dots of CSF signal <3 mm diameter in the subcortical gray and WM
  best visualised on T2w
can show enlargement which is thought to indicate glymphatic dysfunction
much easier to see on 7T than 3T
Granberg, T. J Neurol 267, 3199–3212 (2020).

## Slide 8: CSF and ISF
CSF
  highly vascularised tissue located in ventricles that produces CSF
ISF
  brings oxygen and nutrients to cells and clears away waste
The mixing of CSF and ISF in vital to the waste clearance function of the glymphatic system

## Slide 9: CSF dynamics
flow of CSF into brain is caused by
  constant pressure of production of new CSF
  pulsation of the heart drives CSF into the periarterial spaces
CSF influx is increased during sleep
CSF movement is considered pseudorandom with a turbulent flow component and a molecular diffusion component

## Slide 10: MRI in Neurofluids

## Slide 11: MRI methods to evaluate glymphatic system
Agarwal N JMRI 2024

## Slide 12: Gadolinium Based Contrast Agent (Gold standard)
Intrathecal
First studies done on animals with injection of tracer and two photon laser microscopy1
evaluates the pathway opposite to drainage of brain waste
difficult to use in deep white matter
not approved for use in humans
Intravenous
used to measure BBB leakage
  can also enhance PVS
1Iliff JJ. Sci Transl Med. 2012

## Slide 13: Diffusion Tensor Imaging of Neurofluids
CSF > extracellular water > intracellular water
(~unrestricted) (intermediate) (restricted within the cell)
Low b-values (<500 s/mm2): signal sensitive to water movement in the tissue microstructure, including CSF along PVSs
Low to intermediate b-values: measure pseudorandom motion of CSF or capillary blood flow.
Intermediate b-values (~1000 s/mm2): provide insights into tissue structure and integrity (single-shell DTI and DTI-ALPS)
Very high b-values (>3000 s/mm2): sensitive to restricted diffusion within cellular structures

## Slide 14: DTI methods
Intravoxel incoherent motion (IVIM)
  broad range of b-values (emphasis on intermediate b)
DTI analysis along the perivascular space (DTI-ALPS)
  relies on anatomical features of PVS at level of lateral ventricle
model multi-shell DTI into 3 components
  diffusion, perfusion and intermediate flow reflecting CSF/ISF
low b-value DTI
  sensitive to unrestricted fluid in large spaces like CSF

## Slide 15: Intravoxel Incoherent Motion (IVIM)
a range of low to intermediate b-values has the potential to provide increased specificity
diffusion model that incorporates additional sources of dephasing beyond molecular diffusion, including incoherent flow such as that found in CSF
range of b-values and biexponential fit allows for the separation of a fast pseudo-diffusion and slow molecular diffusion compartment
  signal from the fast compartment could have multiple sources including the microvasculature, CSF, or the ISF
Le Bihan D. Radiology. 1986

## Slide 16: Free Water Fraction (FWF) Diffusion
initially proposed to disentangle the diffusion signal of extracellular free water from that of tissue compartments
single-shell protocols using a dual compartment model to estimate parenchymal FWF
using the same 2-compartment model but with a multi-shell acquisition gives more accurate measures
increased diffusivity measures in the morning compared to the evening driven by an increase in CSF/ISF-like FWF
  linked to increased glymphatic function during sleep

## Slide 17: DTI aLong the Perivascular Space (DTI-ALPS)
Lee DA. Epilepsia Open. 2022

## Slide 18: Diffusion Kurtosis Imaging
accounts for non-Gaussian diffusion within the tissue microenvironment
uses high b-values (>1500 s/mm2)
Changes in kurtosis may reflect alterations in the intracellular and extracellular environment caused by glymphatic function

## Slide 19: Low b-value (<200–500 s/mm2)
sensitive to a combination of incoherent flow and molecular diffusion,
low b-value diffusion coefficient can detect the directional dependence of fluid movement in the PVS parallel to the direction of arterial blood flow
  dependent on the cardiac cycle, with an increase of 300% measured during diastole
Two distinct CSF compartments found
  lateral ventricles: pseudo random diffusion
  3rd and 4th ventricles and sylvian fissure: linear or directional flow

## Slide 20: low-b DTI
used to measure pseudorandom flow of CSF
Y Bito 2021 MRM

## Slide 21: low-b DTI - acquisition
Diffusion-weighted echo-planar imaging:
  TR = 10 s
  TE = 90 ms
  field of view = 240 mm (set to cover CSF at the top of head)
  matrix = 128 x 128
  slice thickness = 4 mm (interpolated to 2 mm)
  number of slices = 30 (interpolated to 59).
  diffusion gradients pulses: δ = 22.8 ms, Δ = 43.6 ms, diffusion time τd = 36.0 ms, and b = 0/100/1000 with 15 noncolinear directions
  acquisition time = 5 min 10 s.
  3T Hitachi scanner
Y Bito 2021 MRM

## Slide 22: low-b DTI - analysis
2 tensors calculated
  low b-value 0-100 (DTL)
  high b-value 0-1000 (DTH)
calculate MD and FA
visually select ROI in CSF
  high MD and FA
  low MD and FA (free water reference)
Y Bito 2021 MRM

## Slide 23: Details from a recommended manuscript

## Slide 24: low-b DTI - dataset
OASIS-3
  mix of controls and cognitively impaired participants
  66 gradient directions
  b-values
    100 s/mm2 (16 directions)
    250 s/mm2 (10 directions)
    500 s/mm2 (12 directions)
    1,000 s/mm2 (12 directions)
    1,500 s/mm2 (10 directions)
    2,000 s/mm2 (6 directions)
    3 b0

## Slide 25: low-b DTI - analysis
CSF pseudo-diffusion spatial statistics (CΨSS)
correction for Gibbs ringing - mrdegibbs (MRtrix3)
correction for eddy currents - eddy_correct (FSL)
Fit low b-value to the DTI model to extract CSF mean pseudo-diffusivity (MΨ)
  also fit intermediate and high b-value
FA and MD images segmented into WM and CSF
  used to create pseudo-T1w images
Atlases created of MΨ and pseudo-T1 (ANTs)

## Slide 26: low-b DTI - analysis
Seed based correlation
ROIs defined
  premedullary cistern,
  cerebral aqueduct-4th ventricle
  foramina of Monro,
  right and left Sylvian fissure
Mean MΨ extracted
Voxel-wise Pearson’s correlations

## Slide 27: low-b DTI - analysis
Non-negative matrix factorization
identify CSF flow patterns where CSF MΨ covaries consistently among participants
Machine learning technique:
https://github.com/asotiras/brainparts
CSF Waterways (CWW)

## Slide 28: Questions and Discussion

## Slide 29: Next Meeting
Wednesday, Feb 4th
Topic ?