## Slide 1: Arterial Spin Labeling
Irene Vavasour
Mar 6, 2024
UBC MRI Research Monthly Analysis Meeting

## Slide 2: References
P Clement, J Petr, MBJ Dijsselhof, et al. A Beginner’s Guide to Arterial Spin Labeling (ASL) Image Processing. Frontiers in Radiology. 2022;2:929533.
L Hernandez-Garcia, A Lahiri, J Schollenberger. Recent Progress in ASL. Neuroimage 2019;187:3-16.
Alsop DC, Detre JA, Golay X, et al. Recommended implementation of arterial spin-labeled perfusion MRI for clinical applications: A consensus of the ISMRM perfusion study group and the European consortium for ASL in dementia. Magn Reson Med 2015;73(1):102–116.
ASL resources prepared by OSIPI (ISMRM ASL Study Group) can be found at https://osipi.github.io/

## Slide 3: What is Arterial Spin Labeling (ASL)
MRI technique for brain perfusion measurements
Advantages over more widely used dynamic-susceptibility contrast (DSC) MRI or PET
  no exogenous contrast agent
    avoids side effects
    cheaper
    immediately repeatable
  labeled water not confined to intravascular spaces

## Slide 4: Cerebral Blood Flow
Cerebral blood flow (CBF) is dependent on
  heart rate
  blood pressure
  blood volume
  blood composition
    hematocrit
    vessel anatomy
  oxygen metabolism (neurovascular coupling)
In young healthy adults, CBF values:
  cortical grey matter = ~50-70mL/100g/min
  white matter = ~20mL/100g/min

## Slide 5: ASL Acquisition
Labeling
-inflowing blood magnetisation is inverted
Post-Labeling Delay (PLD)
- allows blood to flow into vessels and capillaries
Acquisition
- a control and labeled image are subtracted
M0 image
- perfusion calibration image acquired for quantification
Structural Image
- allows ROI analysis

## Slide 6: ASL Acquisition
T Iutaka. RadioGraphics 2023
CBF =
6000*λ*(Scontrol-Slabel)*ePLD/T1,blood
2*α*T1,bloodSPD*(1-e-t/T1,blood)
partition coefficient
efficiency of labeling

## Slide 7: ASL Acquisition
Difference between control and labeled signal is ~1-2% so need averaging
Can also do background suppression
  extra RF pulse between labeling and acquisition to reduce tissue signal
  Helps reduce the effect of head motion
Newer acquisition protocols collect data at several PLDs
  provides temporal dynamics
  more accurate CBF measurement

## Slide 8: ASL Acquisition
P Clement Frontiers in Radiology 2022
Also have Velocity-selective ASL
inverts spins based on blood velocity, by saturating blood moving faster than predetermined rate
good for slow flow such as in stroke

## Slide 9: ASL signal
Affected by
  labeling efficiency
  T1 relaxation in arterial blood
  blood transport time through vessels and tissue
  magnetisation transfer effects

## Slide 10: Use of ASL
T Iutaka. RadioGraphics 2023

## Slide 11: Limitations
Perfusion alterations are small
  not visible in individuals
  Can only detect perfusion differences at a group level
Longer acquisition time means more susceptible to motion

## Slide 12: Processing Steps
P Clement Frontiers in Radiology 2022

## Slide 13: Data Conversion and Sharing
Many software pipelines use NIfTI format
Having data in BIDS format also helpful
  ASL-BIDS extension

## Slide 14: Structural Processing
Lesion Filling on 3DT1
  Lesions can be identified on FLAIR and mapped to the 3DT1
  need to fill in lesions to help with subsequent steps
Tissue Segmentation
  segment into WM, GM and CSF
  helps restrict analysis to only brain tissue
  can be used for partial volume correction
Registration to Standard Space
  need to be careful if brains deviate from normal (e.g. older brains with large ventricles or pediatric brains)
*Many of these steps have been reviewed in previously and are available on our github page https://github.com/irenevav/UBC_MRI_Centre_AnalysisHub

## Slide 15: Single-Subject ASL Processing
Pre-processing steps
  motion correction
    fairly critical since this is a subtraction technique
    can be difficult with the low SNR raw images
    M0 image or middle ASL timepoint used as reference
      affine registration
      normalised correlation as similarity metric
      trilinear interpolation
  outlier exclusion
    remove images with excessive artefacts or other issues
    note, in 3D acquisitions, there are fewer control-label pairs so no exclusion done
  registration
    registration of ASL difference image and structural image
      use grey matter probability maps
      cost function of mutual information
      cubic b-spline interpolation
  M0 processing
    used for voxel-wise calibration and B1 correction
Pre Post

## Slide 16: Single-Subject ASL Processing
CBF Image Quantification
  calculated by subtracting the label from the control images
  M0 used to quantify values in mL/100g/min
  For 2D imaging, do slice time correction in addition to PLD time
  With a single PLD, the delay needs to be longer than the arterial transit time (ATT). If not can get
    macrovascular artefacts
    signal voids
  hematocrit levels can affect CBF estimation
    can estimate blood T1 from the hematocrit value but usually quite noisy measure

## Slide 17: One-compartment CBF model
assumes blood enters through artery and exchanges with the tissue immediately and fully
  i.e. uses fast exchange between compartments
assumes that blood has stayed intravascular and decayed with a blood T1 ~1.65s (at 3T)
  protons spend some time in blood and some time in tissue
    blood T1 and tissue water T1 are not equal
assumes all blood in artery exchanges with tissue
  only a portion does so

## Slide 18: Two-compartment CBF model
accounts for signal from
  intravascular water
  extravascular water
  exchange
New sequences such as diffusion-weighted or multi-echo time ASL can use this model to measure transport across BBB
Characterised with
Multi-TE PLD pCASL
A Paschoal. ISMRM 2023

## Slide 19: Single-Subject ASL Processing
Partial Volume Correction
  CBF in GM is 2-4X higher than WM
  more of a problem because of ASL’s low spatial resolution (4x4x4mm3)
  can lead to underestimation of GM CBF
  estimate the GM CBF in each voxel by regressing out the GM and WM volumes from the CBF map

## Slide 20: Group-Level Processing
create a template
create masks
  excluded unwanted regions that may mess with the analysis
    outside of brain
    signal dropout from susceptibility
    areas of vascular fluctuations
Multi-sequence equalisation
  normalisation of CBF values over multi-site data
ROI statistics
  usually includes whole brain, GM and specific ROIs of interest
  make sure the region is large enough because of ASL’s low resolution

## Slide 21: Outputs from ASL analysis
cerebral blood flow (CBF) map
bolus arrival time (BAT)
arterial transit time (ATT)
mean transit time (MTT)

## Slide 22: ASL software packages
For a list of software visit https://osipi.github.io/task-force-1-1/
I’m going to go over a few of the more used ones
  ASLPrep: A Robust Preprocessing Pipeline for ASL Data
  BASIL: Bayesian Inference for Arterial Spin Labeling MRI
  ASLtbx
  ExploreASL

## Slide 23: ASLPrep
developed by the Satterthwaite lab at the University of Pennsylvania
uses a combination of tools from well-known software packages, including FSL, ANTs, FreeSurfer and AFNI
Info found at https://aslprep.readthedocs.io/en/latest/
largely based on fMRIprep

## Slide 24: BASIL
Found in FSL toolbox (6.0.1)
Good for use in multi-PLD
For functional experiment with ASL data, i.e. one where you want to use a GLM, consult perfusion section of FEAT,
For dual-echo (combined BOLD and ASL) data, consult FABBER.
visit https://fsl.fmrib.ox.ac.uk/fsl/fslwiki/BASIL for details on what’s available and how to use

## Slide 25: ASLtbx
https://www.cfn.upenn.edu/zewang/ASLtbx.php
can be used for both resting ASL data processing and ASL perfusion fMRI data processing
based in Matlab 5.3 and SPM 5/8/12
Looks like it hasn’t been updated since 2015.

## Slide 26: ExploreASL
aim was to develop a comprehensive pipeline for reproducible multi-centre ASL analysis
part of NITRC neuroimaging pipelines https://www.nitrc.org/projects/exploreasl/
can be installed as a docker package or can be used within Matlab
code found at https://github.com/ExploreASL/ExploreASL/
description of the pipeline and code is in this paper
https://doi.org/10.1016/j.neuroimage.2020.117031
uses MATLAB and SPM12

## Slide 27: ExploreASL

## Slide 28: Next Meeting
When: Wed Apr 3rd, 3:15-4:15
Where: CBH 3502 or zoom
Topic: Magnetisation Transfer