## Slide 1: Using Spinal Cord Toolbox for image analysis
Irene Vavasour
Oct 1, 2025
UBC MRI Research Centre Monthly Analysis Meeting

## Slide 2: Difficulties with spinal cord imaging and analysis
small size
  13mm in diameter
deformable
  cord can change shape depending on position of neck and head
motion
  cord and CSF motion with heart pulsation
  motion from swallowing
susceptibility
  surrounded by bone and other organs
Lack of distinct features
  hard to register since cord is mainly a simple cylinder so levels are not distinct

## Slide 3: Spinal Cord Toolbox (SCT)
open-source command-line tools for spinal cord MRIs
created by Dr. Julien Cohen-Adad’s group (PolyLab) at Ecole Polytechnique de Montreal
latest release version 7.1
works on Linux, macOS and Windows
Reference: De Leener B, Lévy S, Dupont SM, Fonov VS, Stikov N, Louis Collins D, Callot V, Cohen-Adad J. SCT: Spinal Cord Toolbox, an open-source software for processing spinal cord MRI data. Neuroimage. 2017 Jan 15;145(Pt A):24-43.
Website: https://spinalcordtoolbox.com/stable/

## Slide 5: Best acquisitions for SCT
T2 - shows good contrast between cord and CSF
  T1 and T2* can also be used in some pipelines
  SCT is trying to develop contrast agnostic tools

## Slide 6: Segmentation
usually done on T2w images
  but can use other contrasts although cross sectional area (CSA) may differ if using different contrasts (although this is becoming less of a problem with newer tools)
command is sct_deepseg
example: sct_deepseg spinalcord -i t2.nii.gz -qc ~/qc_singleSubj

## Slide 7: Segmentation
sct_deepseg spinalcord -i t2.nii.gz -qc ~/qc_singleSubj
can replace spinalcord with
  graymatter
  lesion
  rootlets
  …
SCT uses a deep learning model to do the segmentation
  can see info on model with deep_seg -task-details

## Slide 8: Grey Matter segmentation
uses a slightly different algorithm
sct_deepseg_gm
example
  sct_deepseg_gm -i t2s.nii.gz -qc ~/qc_singleSubj

## Slide 9: White Matter Segmentation
subtract the GM from the whole cord segmentations
sct_maths -i t2s_seg.nii.gz -sub t2s_gmseg.nii.gz -thr 0 -o t2s_wmseg.nii.gz

## Slide 10: Lesion Analysis
segment (in SCT v7.0 or higher) with
  sct_deepseg lesion_sci_t2 (for spinal cord injury)
  sct_deepseg lesion_ms (for MS lesion)
  sct_deepseg lesion_ms_axial_t2 (for MS lesion on T2 axial images)
  sct_deepseg lesion_ms_mp2rage (for MS lesion on cropped mp2rage)

## Slide 11: Lesion analysis
After segmentation, can do morphometric measures
  eg. volume, length, max diameter, width, …
command:
sct_analyze_lesion -m t2_lesion_seg.nii.gz -s t2_sc_seg.nii.gz -qc qcname
can also do template analysis of lesions
  proportion of ROI occupied by lesion
  proportion of lesion within each vertebral level or tract

## Slide 12: Registration to PAM50 template

## Slide 13: Registration
sct_register_to_template
  This algorithm does:
    straightening
    vertebrae-matching transformation
    shape matching transformation
example:
  sct_register_to_template -i t2.nii.gz -s t2_seg.nii.gz -l t2_labels_vert.nii.gz -c t2 -qc ~/qc_singleSubj

## Slide 14: Vertebral Labelling
Needed for registration step
labels are placed as though the vertebrae were projected onto the spinal cord, with the label centered in the middle of each vertebral level
sct_label_vertebrae automatically labels
example: sct_label_vertebrae -i t2.nii.gz -s t2_seg.nii.gz -c t2 -qc ~/qc_singleSubj
This step sometimes fails so need to manually label C2-C3 level

## Slide 15: Manual Vertebral Labelling
sct_label_utils -i t2.nii.gz -create-viewer 3 -o label_c2c3.nii.gz \
-msg "Click at the posterior tip of C2/C3 inter-vertebral disc“
sct_label_vertebrae -i t2.nii.gz -s t2_seg.nii.gz -c t2 -initlabel label_c2c3.nii.gz -qc ~/qc_singleSubj

## Slide 16: Registration
can customise the registration with arguments
Default values for '-param’ argument
-param step=1,type=imseg,algo=centermassrot,metric=MeanSquares,iter=10,smooth=0,gradStep=0.5,slicewise=0,smoothWarpXY=2,pca_eigenratio_th=1.6:step=2,type=seg,algo=bsplinesyn,metric=MeanSquares,iter=3,smooth=1,gradStep=0.5,slicewise=0,smoothWarpXY=2,pca_eigenratio_th=1.6
-ref argument
  select destination for registration: template or subject space

## Slide 17: Registration
After finding transformation between subject and template space, can use warp field to move template to subject space
  sct_warp_template -d t2.nii.gz -w warp_template2anat.nii.gz -a 0 -qc ~/qc_singleSubj

## Slide 18: Registration
Can co-register other quantitative images to the template
segment the quantitative image - sct_deepseg
create mask around segmentation - sct_create_mask
registration to template
  option 1: reuse warping field - sct_register_multimodal
  option 2: direct registration to template
    sct_label_utils
    sct_register_to_template
now warp template to subject space - sct_warp_template

## Slide 19: Computing CSA
To compute the cross sectional area (as well as some other parameters) use
  sct_process_segmentation -i t2_seg.nii.gz -vert 2:3 -vertfile ./label/template/PAM50_levels.nii.gz -o csa_c2c3.csv

## Slide 20: Computing quantitative measures
After registering the template to the quantitative imaging space can use
  sct_extract_metric -i mtr.nii.gz -f label/atlas -method map -l 51 -o mtr_in_wm.csv
  -l refers to which ROIs will be used
  50: whole cord
  51: WM
  52: GM
  53: dorsal column
  54: lateral funiculi
  55: ventral funiculi

## Slide 21: Another good reference
Jan Valošek, Julien Cohen-Adad, Reproducible Spinal Cord Quantitative MRI Analysis with the Spinal Cord Toolbox, Magnetic Resonance in Medical Sciences, 2024, Volume 23, Issue 3, Pages 307-315.
  up-to-date review on how best to collect and analyse spinal cord data

## Slide 22: Next Meeting
Wednesday Nov 5th
3:15-415
Topic: ???