## Slide 1: Data formats and formatting data: PAR/REC, dicom, BIDS, …
April 5, 2023

## Slide 2: Data Formats

## Slide 3: PAR/REC
PAR=parameter
  Includes all the header information
REC=records?
  Includes the imaging data
Convert to .nii using dcm2niix
  Note: depending on the version, dcm2niix may or may not scale the images correctly
    For conventional images, the intensity should be in the 106 rather than 103
    Only really matters if combining data from different sequences

## Slide 4: Example PAR file

## Slide 5: Example PAR file

## Slide 6: GE Raw files

## Slide 7: DICOM
Stands for Digital Imaging and Communications in Medicine
Supposed to be a universal file format
  Each vendor is slightly different
    Odd numbered tags can be vendor specific
  Comes in classic and enhanced versions

## Slide 8: Reading Dicoms
Images just saved as a large list
  On philips, data saved in chunks of 2048 files
  On GE, data saved all together in one directory
  Enhanced dicom generally just makes one file
To see header in matlab: dicominfo
  Many other programs available
Convert to .nii using dcm2niix
  Note that version number can be important as features keep changing
  Also note that the json file does not capture all header info (e.g. scan date)

## Slide 9: Example Dicom Header

## Slide 10: NIFTI
Used by many applications and scripts
Not usually a raw data format off scanner
  Convert to .nii using dcm2niix
  Lose some header info after conversion
Note that it’s usually saved in .gz format
  Some applications (e.g. matlab) do not deal with this well

## Slide 11: ISMRM Raw Data Format
The ISMRM Raw Data (ISMRMRD) format is proposed as a common MR raw data format to facilitate the sharing of data and data processing tools.
It is composed of the data fields required to reconstruct images from magnetic resonance experiments.
C/C++, Python and MatLab application interfaces have been developed to translate MR data from the different MR vendors into this open data format.

## Slide 12: ISMRMRD
The data is stored in HDF5 format combining a mix of flexible and fixed data structures in the next way:
  A flexible document that can contain an arbitrary number of fields in an XML format. This document stores parameters that are specific to the experiment.
  A raw data section that holds the data acquired from the experiment.
  Additional post-processed data, such as reconstructed images and coil sensitivity maps, can be stored in the HDF5 header.
Reference: Inati SJ, Naegele JD, Zwart NR, Roopchansingh V, Lizak MJ, Hansen DC, Liu CY, Atkinson D, Kellman P, Kozerke S, Xue H. ISMRM Raw data format: A proposed standard for MRI raw datasets. Magnetic Resonance in Medicine. 2016 Jan 1.

## Slide 13: Formatting data

## Slide 14: What is BIDS
BIDS (Brain Imaging Data Structure) is a standardized format for organizing and describing neuroimaging datasets to promote re-use of both data and code
BIDS defines a specific directory structure and a precise file naming schema

## Slide 15: MRI data in BIDS
MRI data stored in the NifTI format
  Paired with a JSON sidecar file
Extra .json and .tsv files to describe the entire dataset and relevant participant infomation

## Slide 16: BIDS drawback
BIDS was inspired by the OpenfMRI (OpenNeuro) repository structure.
Therefore the labeling is very fMRI focused making it less attractive to researchers developing new sequences.
  But if you’re the first then you can define how your data should be labeled in BIDS
  New guidelines in the BIDS Extension Proposal 001
    https://doi.org/10.1038/s41597-022-01571-4

## Slide 17: How to convert data to BIDS
BIDScoin
Bidsify
Dcm2Bids
XNAT2BIDS
By hand
  might be necessary for non-standard datasets

## Slide 18: BIDS Filesystem structure
Currently at version 1.8.0
  https://bids-specification.readthedocs.io
Each subject put in subdirectory named “sub-<label>”
  Can add a participants file here for more info
Each session becomes a subdirectory within the participant directory named “ses-<label>”
  Again can add a session file for more info
Next add subdirectories for each data type
  Data types are func, dwi, fmap, anat, perf

## Slide 19: BIDS Filesystem structure
Top level directory must include
  Subject directories
  dataset_description.json
  README
Top level directory may also include:
  Directory for code
  Directory for derivatives
  Directory for sourcedata
  Directory for stimuli
  Participants file (.tsv and .json)
    This file must contain a list of participant IDs, one participant per row

## Slide 20: BIDS filenames
Consists of a chain of entity instances and a suffix separated by underscores, and an extension
  E.g. sub-01_task-rest_bold.nii
  There is a convention to the ordering of the entities

## Slide 21: BIDS metadata
Use .tsv or .json files
The more info the better
Example of participant.tsv
Example of participant.json

## Slide 22: Example Dataset description file

## Slide 23: BIDS derivatives
Filename should not conflict with raw files
Filename form:
  <source_entities>[_keyword-<value>]_<suffix>.<ext>
If necessary to distinguish 2 files with no other differences use _desc-<label>
  E.g. different pre-processing steps
Again use .json files to describe the data (including what source data was used)

## Slide 24: BIDS Extension Proposals
BEP001 for qMRI
  https://github.com/bids-bep001/bids-specification

## Slide 25: BIDS notation for qMRI

## Slide 26: Extra BIDS filename notations

## Slide 27: Example BIDS structure for qMRI
Raw Data
Processed Data

## Slide 28: Citing BIDS (original publication)
Gorgolewski, K.J., Auer, T., Calhoun, V.D., Craddock, R.C., Das, S., Duff, E.P., Flandin, G., Ghosh, S.S., Glatard, T., Halchenko, Y.O., Handwerker, D.A., Hanke, M., Keator, D., Li, X., Michael, Z., Maumet, C., Nichols, B.N., Nichols, T.E., Pellman, J., Poline, J.-B., Rokem, A., Schaefer, G., Sochat, V., Triplett, W., Turner, J.A., Varoquaux, G., Poldrack, R.A. (2016). The brain imaging data structure, a format for organizing and describing outputs of neuroimaging experiments. Scientific Data, 3 (160044). doi:10.1038/sdata.2016.44

## Slide 29: BIDS Starter Kit
Contains a collection of tutorials, wikis and templates
  https://bids-standard.github.io/bids-starter-kit/

## Slide 30: Next Meeting
Wednesday May 3rd
Topic: