## Slide 1: Preparing your data for fMRI analysis
Irene Vavasour
Nov 1, 2023
UBC MRI Research Monthly Meeting

## Slide 2: Disclosure
Most of the information for this presentation was grabbed from the May 2023 fMRI Brain Camp:
  Co-organisers: Dr. Justin Andrushko, Andre Zamani and Dr. Daniela Palombo
  Teaching assistants: Chantelle Cocquyt, Brandon Forys, Jacqueline Lee, Jen Burrell
Thank-you to all the organisers. It was an excellent course and I learned a lot.
This will be a somewhat condensed version hitting mainly the highlights.
Lastly, I will again note that I’m not an expert at fMRI or fMRI analysis.

## Slide 3: Blood Oxygen Level Dependent (BOLD) signal
reflects changes in deoxyhemoglobin (paramagnetic) driven by localised changes in brain blood flow and blood oxygenation
  coupled to underlying neuronal activity
When a region of the brain is activated, the increased neural firing and other signaling processes result in a locally increased energy requirement
Increased blood flow acts to restore local O2 levels required to overcome the transient deficit; however, more oxygen is delivered than needed
  Known as the hemodynamic response

## Slide 4: 2 Types of fMRI studies
task-based fMRI
  Participant is asked repeatedly to do a task followed by a rest period (on-off-on-…)
  Analysis compares the BOLD signal while doing the task vs rest
resting-state fMRI
  Participant lies in the scanner not thinking of anything in particular while the sequence is being run (min 8 minutes)
  Analysis compares the BOLD signal pattern across brain regions

## Slide 5: fMRI sequences
 | Philips | GE PETMR | GE MR only
Coil | dSTREAM 32 channel | HNU 12 channel | HNU 12 channel
Orientation | Axial Oblique | Axial(PETMR) | Axial/Axial oblique(MR only)
FOV (mm) | 240 | 258 | 258
Slice thickness (mm) | 2.5 | 3 | 3
#Slices | 62 | 62 | 62
Matrix | 96 | 86 | 86
Voxel size FxPxS (mm) | 2.5x2.5x2.5 | 3x3x3 | 3x3x3
TR (ms) | 2000 | 2000 | 2000
TE (ms) | 30 | 25 | 25
Flip angle (deg) | 77 | 77 | 77
Parallel Imaging Factor | 2 | 2 | 2
Multiband factor | 2 | 2 | 2
Acquisition time | 8-15 min | 8-15 min | 8-15 min
rsfMRI
task based fMRI
TR = 1-3s
TE = ~30ms
voxel = 2.5x2.5x2.5mm3
EPI factor = 13-39
Multi-echo
TR = 2s
TE = 12, 24.5, 37ms
voxel = 3x3x3mm3
EPI factor = 19
Sequence is echo planar imaging (EPI) sensitive to T2* relaxation

## Slide 6: Things to think about
When scanning, to know your orientation for sure, place a vitamin E capsule on one side of the head
  sometimes orientations can get messed up in the data header files which is a nightmare to try to figure out
Make sure you get your sequence parameters from the scan
  some will be important in the analysis
Recommend putting you data in BIDS format
  some of the analysis code will expect data to be in BIDS format

## Slide 7: Structural Preprocessing

## Slide 8: Structural Data Preprocessing Steps
Correct Orientation
Cropping
Bias Field Correction
Brain Extraction
Tissue Segmentation
Subcortical Segmentation
Note: All these steps are done on the 3D T1w images

## Slide 9: Correct Orientation
Images are normally reoriented to make sure they are in standard (i.e. MNI template) orientation
  This will be an axial slicing of the data
fslreorient2std input.nii.gz output_std.nii.gz

## Slide 10: Cropping
Want to remove unwanted parts of the image (e.g. neck) for better brain extraction and segmentation down the line
robustfov -i input_std.nii.gz -r output_std_fov.nii.gz
Before
After

## Slide 11: Bias Field Correction
Improves the signal homogeneity across the image
  Note: Be wary of using this on quantitative images
Can use a variety of programs including
  N4BiasCorrection in ANTs
  N4BiasFieldCorrection -d 3 -i filename.nii.gz -o outfilename_N4.nii.gz
  FAST in fsl
  fast -B -b --nopve -o output input_std_fov.nii.gz

## Slide 12: Brain Extraction
Removes the skull and non-brain tissue
bet input_N4.nii.gz output_N4_brain -R -f 0.2 -B
Options:
-R more robust iterative method (but takes longer)
-f fractional intensity threshold; default=0.5; smaller values remove less brain
-B runs bias field correction so no need to do previous step

## Slide 13: Tissue Segmentation
Segments the brain into white matter, grey matter and CSF
  might want to limit analysis to GM where BOLD signal is thought to predominate
  fast -o output input_biascorr_brain.nii.gz
Outputs will be partial volume maps (_pve_#) for each tissue type

## Slide 14: Subcortical Segmentation
Segment the subcortical brain structures
  Structures are: thalamus, caudate, putamen, pallidum, brain stem, hippocampus, amygdala, accumbens
  FAST does not do a good job of this segmentation
  run_first_all -d -b -v -i input_biascorr_brain.nii.gz - output
Options
-b indicates input is already brain extracted
-d do not delete intermediate files
-s list of specific structures to segment (one structure or csv file)

## Slide 15: Preprocessing pipeline
These preprocessing steps are put into a semi-automated pipeline in
anat_preprocessing_v1_1.sh
found at https://github.com/irenevav/UBC_MRI_Centre_AnalysisHub
or a fully automated pipeline
fsl_anat

## Slide 16: Functional Preprocessing

## Slide 17: Next steps: Functional Data Preprocessing
Motion Correction
Susceptibility Distortion Correction
Slice Timing Correction
Brain Extraction
High Pass Filtering
Manual ICA Denoising
Spatial Smoothing
Normalisation

## Slide 18: Motion Correction
Register all the fMRI volumes within the scan to a reference image
  mcflirt -in input_bold.nii.gz -out output_bold_mcf.nii.gz

## Slide 19: Susceptibility Distortion Correction
Shape of the brain can be distorted when using a fast EPI sequence
Two methods for correction:
  fieldmap
    collect an extra scan of the Bo field
    use FSL FEAT to correct EPI images
SE-EPI_A Anterior >> Posterior
SE-EPI_P Posterior >> Anterior
  topup
    requires an extra dataset collected with the reverse phase-encoding direction
    Generally 2 spin-echo EPI sequences are collected, one with each phase-encoding direction

## Slide 20: Topup
create acq_params.txt file:
fslmerge -t output_bold_PA_AP_B0 input_epi_PA input_epi_AP
topup --imain= output_bold_PA_AP_B0 --datain=acq_params.txt --config=b02b0.cnf --out=_rs_topup --fout=_topup_field
applytopup --imain=input_bold --inindex=1 --method=jac --datain=acq_params --topup=…_rs_topup --out=output_bold_corrected
Note: topup requires an even number of slices to run
0 -1 0 TotalReadoutTime
0 1 0 TotalReadoutTime
Anterior ← Posterior = 1
Anterior → Posterior = -1
Echo Spacing * 0.001 * EPI factor

## Slide 21: Slice Timing Correction
Interleaved slice acquisition is preferred to diminish cross talk between slices
Spatially adjacent slices are not acquired at the same time so need to correct for this
Use information from nearby timepoints to interpolate the BOLD signal relative to a reference timepoint
  can introduce ringing effects and noise spreading
At short TRs, not as necessary
Finicky to do with multiband data

## Slide 22: Brain Extraction
Similar to previous BET step but -f factor may need to be modified
Can also use bet to create a whole brain mask to be used later
  use the -m option

## Slide 23: Temporal Filtering
3 filter types
  high-pass
    allows high frequencies through but not low frequencies (e.g. cardiac and breathing motions)
  low-pass
    allows low frequencies through but not high frequencies
    not recommended
  band-pass
    attenuates both high and low frequencies
Shorter TRs can help resolve physiological noise
  Shorter TR = higher sampling rate
  Increased noise via multiband effects
  Increased autocorrelation (physiological cleaning helps)

## Slide 24: Denoising
One method is independent component analysis (ICA)
  ICA groups data into components that are least correlated with each other
  These components will resemble sources of signal, noise or both
Noise
Motion
Tissue of no interest
Physiological effects
artefacts
Mixed
Task-correlated motion/signal
Vasculature and signal
Multiband and signal
Signal
BOLD effect

## Slide 25: Denoising: Example Noise Components

## Slide 26: Denoising
Timeseries
Timeseries
Power Spectra
Power Spectra

## Slide 27: ICA Denoising
Pros
  fairly robust separation of signal and noise
  can keep mixed components rather than just throwing away anything with motion contamination
    less aggressive denoising
Cons
  subjective classification of components
Software for ICA denoising
  ICA-AROMA (fully automated)
  ICA-FIX

## Slide 28: Denoising
After categorising the components as signal, noise or both, we regress out the noise
  best to use non-aggressive partial regression to only remove true noise (and keep mixed signal)
fsl_regfitl -i filtered_func_data -o denoise_data -d filtered_func_ data.ica/melodic_mix -f “#,#,#”
component numbers labelled as noise

## Slide 29: Spatial Smoothing
Reduce high frequency spatial components
Helps with multiple comparison problem
Increases SNR per voxel
Usually use a gaussian filter with width from 4-8mm
Important not to over smooth or might lose signal differences
Decisions of smoothing are dependent upon data quality, preprocessing steps and intended analyses

## Slide 30: Spatial Normalisation
Move each participant brain into a “standard space”
  MNI most used standard space
Usually done in 3 steps
  register functional to structural
  register structural to standard
  concatenate registration matrices to bring functional to standard
Remember though that normalisation does not equal 1 to 1 voxel matching
  In pathological and older brains (large ventricles) this is even more true
There is a great deal of individual variation in brain organisation

## Slide 31: Even more processing steps possible
Linear detrending
Despiking
Intensity normalization
Nuisance regression
And more…

## Slide 32: Order of processing debate
The order in which some of these steps are done is still under debate
  The order I present here (in bold) is based on what the fMRI brain camp suggested
Motion correction before or after distortion correction
Slice timing correction vs. modelling a temporal derivative
Filtering before or after data denoising via independent component analysis
Highpass filtering vs bandpass filtering
Smooth data before or after denoising
Registration: move functional data to structural space or structural data to functional space

## Slide 33: Preprocessing using FEAT
FSL has a package that does the preprocessing steps in a gui
  called FEAT
Feat &
There are a lot of things to set-up which were described in the fMRI brain camp. If you want to go this route I would suggesting attending the next camp
Feat also allows you to do subject level statistics

## Slide 34: fMRIprep: another preprocessing pipeline
more automated but less customisable than fsl
provides a reuseable framework for analysis
install as docker or singularity container
fmriprep input_BIDS_data/ output_dir/ participant –w working_dir/

## Slide 35: Next Meeting
When: Nov 29th
Time: 3:30-4:30pm
Topic: Magnetic Resonance Spectroscopy Analysis with LCModel