## Slide 1: Magnetic Resonance Spectroscopy Analysis with LCModel
Irene Vavasour
Nov 29, 2023
UBC MRI Research Monthly Meeting
And Big Thank-you to Erin for many of the slides!

## Slide 2: Magnetic Resonance Spectroscopy

## Slide 3: What can we detect with MRS?
3T MRS can detect chemicals involved in…
Neuronal “integrity”:
  N-acetylaspartate (NAA)*
Cell energetics:
  Creatine & phosphocreatine (tCr)
  Lactate
Membrane turnover:
  Choline compounds (Cho)
  Lipids
Glial cell density:
  Myo-inositol (mI)
de Graaf. In Vivo NMR Spectroscopy: Principles and Techniques, 2019
*Nordengen et al. Brain Struct Funct 2015
Lipids
NAAG
NAA
Lactate
Glu
Gln
NAA
tCr
Cho
mI
tCr
mI
[Water]
GABA
6.0
5.0
4.0
3.0
2.0
1.0
ppm
Glu
Gln
GSH

## Slide 4: What can we detect with MRS?
de Graaf. In Vivo NMR Spectroscopy: Principles and Techniques, 2019
*Nordengen et al. Brain Struct Funct 2015
Lipids
NAAG
NAA
Lactate
Glu
Gln
NAA
tCr
Cho
mI
tCr
mI
[Water]
GABA
6.0
5.0
4.0
3.0
2.0
1.0
ppm
Glu
Gln
GSH
3T MRS can detect chemicals involved in…
Neurotransmission:
  N-acetylaspartylglutamate (NAAG)
  γ-aminobutyric acid (GABA)
  Glutamate (Glu)
  Glutamine (Gln)
Anti-oxidant reserve:
  Gluthione (GSH)

## Slide 5: Acquisition of MRS
Water Suppression
Data Processing
FFT
Quantification
Localization
MRS voxel
Export data
Fitting
Freq Align
Average

## Slide 6: Water Suppression
[H2O] ~5000x > [NAA]
x100

## Slide 7: Water Suppression
Necessary to remove overlap of water tail and metabolites
Modern scanners cannot handle the dynamic range
Cannot sensitively measure metabolites at the same time as water
Several water suppression options:
Inversion
Excitation
VAriable Pulse powers and Optimized Relaxation delays (VAPOR)

## Slide 8: Voxel Localisation
Several localization options:
Point RESolved Spectroscopy (PRESS)
Stimulated Echo Acquisition Mode (STEAM)
Localization by Adiabatic Selective Refocusing (LASER)
Image Selected In vivo Spectroscopy (ISIS)

## Slide 9: Semi-laser MRS localisation acquisition
4 adiabatic full passage pulses – longer TEs
Adiabatic pulses - sharp chemical shift displacement
RF
Gx
Gy
Gz
90°
Selective
Adiabatic Full Passage
echo
TE
…TR
NAA
Cr

## Slide 10: MRS data pre-processing
Goal: improve spectral quality prior to fitting
Fitting algorithms are very sensitive to spectral quality
Export each individual shot
Phase and frequency alignment
Averaging
Measures of spectral quality:
SNR=
Linewidth: Full width at half maximum (FWHM)
÷ SD[ ]
FWHM
6.0
5.0
4.0
3.0
2.0
1.0
ppm

## Slide 11: MRS spectral fitting (LCModel)

## Slide 12: LCModel
Created by Stephen Provencher
uses a linear combination of basis sets to fit the spectrum
the area under each individual metabolite spectrum is related to the concentration
Download information and manuals can be found here:
http://s-provencher.com/lcmodel.shtml

## Slide 13: To run LCModel
.lcmodel/lcmgui &
Pick the metabolite file (_met.SDAT or _act.SDAT)
Make sure your basis set matches your localisation technique and TE
Location to save data
Look here to edit Control Parameters

## Slide 14: Using LCModel
key=210387309
Parameters to modify
atth2o=1
attmet=1
subbas=F
key=210387309
wconc=1
choose reference file (_wat.SDAT or _ref.SDAT)

## Slide 15: LCModel output

## Slide 16: Absolute Quantification
The values that come out of LCModel do not take into account water relaxation times and differences in tissue concentrations

## Slide 17: Tissue segmentation
The concentration of metabolites is different in WM, GM and CSF so need to correct
Steps
Segment the brain into WM, GM, CSF (and lesion)
  I usually use FAST from FSL on the 3DT1
Localise the MRS voxel onto the 3DT1
  We’ve been using some Philips matlab code to do this but recently also implemented it using a python package called suspect
Extract the fraction of WM, GM, CSF (and lesion) within the MRS voxel

## Slide 18: Calculating WCONC
MRS voxel fractions of tissue
Expected tissue water contents taken from literature1
WCwm = 76.4%
WCgm = 82.0%
WCCcsf = 99.0%
WCMS_lesion = 82.7%
1MacMillan et al. MSJ 2015

## Slide 19: Calculating ATTH2O
 | White Matter | Grey Matter | CSF | MS Lesion
T1 (s) | 1.00 | 1.42 | 3.00 | 1.23
T2 (ms) | 70 | 75 | 500 | 93
Literature values for water relaxation times1
1MacMillan et al. MSJ 2015

## Slide 20: Metabolite relaxation effects
Metabolites also have different relaxation times but usually the values are not know
To minimise effect:
  use long TR
    ≥4s
  use short TE
    ~35ms

## Slide 21: Error measurement
LCModel outputs a Cramer-Rao Lower Bounds as a %SD
  Often a cut off of 20%-30% is used say data is OK
But this value will be dependent on the mean so could bias the results for higher concentrations
  better to use absolute error (AE) = CRLB% * [metabolite]
  reject anything with an AE higher than 30% of the median concentration value from all participants1,2
1MacMillan et al. Mult Scler J Exp Transl Clin, 2019. 2Kreis Magn Reson Med, 2016.

## Slide 22: Other MRS analysis packages
LCModel has been the go to analysis package for MRS for many years but Provencher has retired so no new updates will be made
Many other analysis packages
  Tarquin
  Gannet
  Osprey
  JMRUI
  FSL-MRS (new but combines the FSL tools with MRS)
  …

## Slide 23: Multi-nuclear MRS
Upgrades to the Philips scanner in Dec 2023 will allow multi-nuclear capabilities
  23Na and 31P available
  13C, 129Xe, 19F if someone buys the coil

## Slide 24: Next Meeting
When: Feb 7th
Time: 3-4pm (or maybe 3:15-4:15)
Topic: Artefacts